## Slide 1: Cloud-to-nRF52 DFU
SLM AT Command-based Solution
v0.5
Jun Qing Zou

## Slide 2: Why We Do It
Need a friendly DFU function to work with nRF52 MCU
  nRF52 app developed with legacy SDK or NCS
  Since LTE is available, FOTA over BLE change to FOTA over LTE (naturally)
    No longer need of DFU Controller on PC or phones
  SLM is UART based, ideal to perform Serial DFU protocol
  For NCS nRF52 target, use a simple DFU Download protocol
Using SLM means customer do “zero” development on nRF91
  Out-of-box solution required for firmware update
    nRF91 modem and application (SLM itself) FOTA, existing AT#XFOTA
    nRF91 can use serial DFU method to update nRF52
nRF52 MCU have full control of the DFU process
  AT-based control on
    When to download DFU image
    When to run DFU protocol
  MCU decide when to activate new image
Solution could be ported to non-SLM SoC application

## Slide 3: New SLM AT Commands
Separate HTTP download and DFU over UART into two steps
AT#XDFUGET=<op>,<host>,<image_1>[,<image_2>[,<sec_tag>]]
<op> 0 – cancel download; 1 – download; 8 – erase secondary
<image_1> full path of first image, e.g. init packet in DFU package (save to nRF91 RAM)
<image_2> full path of second image, e.g. file image file in DFU package (save to nRF91 flash)
<sec_tag> for HTTPS, optional
Executed in SLM AT Command mode
Example: AT#XDFUGET=1,"http://myserver.com","/lats/nrf52832_xxaa.dat","/lats/nrf52832_xxaa.bin"
AT#XDFURUN=<start_delay>[,<mtu>,<pause>]
<start_delay> time for nRF52 to get ready for run DFU protocol, in seconds (0 means no delay)
Executed in SLM DFU mode
Example: AT#XDFURUN= 2,1024,200
<host> HTTP(S) server name including port number
Example: AT#XDFUGET=1,"http://myserver.com:80","/lats/nrf52_app_update.bin"
<mtu> 256 * N, 4-byte aligned, size of data chunk sent over UART (NCS nRF52 only)
<pause> Time to wait for nRF52 writing one chunk in milliseconds (NCS nRF52 only)

## Slide 4: Working with nRF5 SDK
SDK 17.0.2 for example

## Slide 5: System View
nRF91 APP
nRF52
nRF52 DFU images (flash / RAM)
SLM/SPM
nRF52 AT app
UART
active application
new image
Download agent & DFU Controller (legacy)
Serial DFU protocol
(bidirectional)
DFU Target (legacy)
HTTP(S)
Web Server
nRF52 DFU
file image
Serial bootloader
Settings
MCUBOOT
PM_MCUBOOT_SECONDARY_ADDRESS or customized partition
APP free space

## Slide 6: Download Design (SLM)
Serial LTE Modem
fota_download
dfu_target
download_client
dfu_target_mcuboot
dfu_target_modem
dfu_target_nrf52
dfu_target_stream
AT#XFOTA=…
AT#XDFUGET=…
Perform HTTP(S) download
Save file_image to flash
SLM FOTA
SLM DFU

## Slide 7: Firmware Changes
nRF91
Serial LTE Modem (SLM)
  Under and CONFIG_SLM_NRF52_DFU CONFIG_SLM_NRF52_DFU_LEGACY
  Serial DFU Controller, courtesy of APAC colleagues
    dfu_host_legacy.c
    slip.c (legacy SDK)
DFU service types
  APP
  SD
  Bootloader
nRF52
Serial bootloader
  Base: SDK_17.0.2\examples\dfu\secure_bootloader
  \pca10056_uart, with HWFC disabled
Sample client app
  Base: SDK_17.0.2\examples\peripheral\libuarte
    Enable UART hardware flow control
      Add gpiote for libuarte too
    Add to issue AT commands
    Change link file to give space for MBR
    Change Makefile to add MBR and missing code
BitBucket repo https://projecttools.nordicsemi.no/bitbucket/projects/CEAP/repos/52_slm_dfu/browse

## Slide 8: How To Test
nRF52 side, only GCC toolchain tested
Build serial bootloader with correct public key
  make, make erase, make flash_mbr, make flash
  NOTE UART HWFC not working well with nRF91 UARTE EasyDMA HWFC
Build original app
  Sign original app and DFU with nrfutil
  NOTE –fc 0 in command line
Build dfu app
  Sign dfu app
  Copy init_packet .dat and file_image .bin to HTTP server
Make sure nRF91 DK VDD IO 3.0V and is powered on when nRF52 run original app
Logic for original app
  Issue AT commands to connect LTE
  Issue AT#XDFUGET=…
  Issue AT#XDFURUN=…
  Jump to serial bootloader right after
SLM
  Project configs to use UART_2 with HWFC
  CONFIG_SLM_NRF52_DFU=y
  CONFIG_SLM_NRF52_DFU_LEGACY=y

## Slide 9: Working with NCS SDK
Master, for example

## Slide 10: System View
nRF91 APP
nRF52
nRF52 DFU image (flash)
SLM/SPM
nRF52 app
UART
active application
new image
Download agent & DFU image server
DFU target
HTTP(S)
Web Server
nRF52 DFU image
MCUBOOT
PM_MCUBOOT_SECONDARY_ADDRESS or customized partition
Download protocol
(unidirectional)
Settings
MCUBOOT
Settings
PM_MCUBOOT_SECONDARY_ADDRESS

## Slide 11: Download Design (SLM)
Serial LTE Modem
fota_download
dfu_target
download_client
dfu_target_mcuboot
dfu_target_modem
dfu_target_nrf52
dfu_target_stream
AT#XFOTA=…
AT#XDFUGET=…
Perform HTTP(S) download
Save file_image to flash
SLM FOTA
SLM DFU

## Slide 12: Download Design (MCU)
nRF52 App
UART RX
dfu_target_stream
AT#XDFURUN=… Stream file_image
Perform UART download
dfu_target_mcuboot
SLM FOTA
SLM DFU

## Slide 13: Firmware Changes
nRF91
Serial LTE Modem (SLM)
  Under CONFIG_SLM_NRF52_DFU
  Serial DFU Host
    dfu_host.c
    MTU/Pause-based transmit control
    CRC32
nRF52 block (4K) erase/write time
  >1s measured by stream_flash_buffered_write()
  DFU host hold on 2s per 4K
DFU service type
  MCUBOOT-based APP FOTA
  MCUBOOT FOTA to be supported
    nRF52 decide B0 or B1 to download
nRF52
Sample client app
  Base: Zephyr HelloWorld
    Add UART (Serial Async) and MCUBOOT
    Add to issue AT commands to
      connect LTE,
      perform file image download
      run DFU download protocol
    Add dfu_ target_mcuboot to receive data and save to secondary partition
      Zephyr stream_flash deferred write
    Reboot to apply new file image
BitBucket repo
  https://projecttools.nordicsemi.no/bitbucket/projects/CEAP/repos/91_slm_dfu/browse

## Slide 14: How To Test
nRF52 side
  Build original app and program DK
  Build dfu app and upload app_update.bin to HTTP server
  Make sure nRF91 DK VDD IO 3.0V and is powered on when nRF52 run original app
Logic from original app
  Issue AT commands to connect LTE
  Issue AT#XDFUGET=,…
  Issue AT#XDFURUN=,…
  Reboot and MCUBOOT update app
  Simple testing bot in one thread
SLM
  Project configs to use UART_2 with HWFC
  CONFIG_SLM_NRF52_DFU=y
  CONFIG_SLM_NRF52_DFU_LEGACY=n

## Slide 15: Optional solution for nRF52 in NCS
Kevin Ai in APAC has ported the serial bootloader in legacy SDK to NCS
  https://github.com/aiminhua/ncs_samples/tree/master/nrf_dfu
  Treat mcuboot update image as legacy FOTA image, use python tool to create download ZIP (init data, file image)
  Run serial DFU protocol and call MCUBOOT to apply the downloaded image
Interactive downloading over UART with error correction

## Slide 16: Protocols Compared
Serial DFU protocol
  Bidirectional, command/response + raw data
  Image size by init packet
  UART driver based
  Flow control by MTU/PRN
  Conversational error control by CRC
    Support re-transmit
  Init packet handles versions, image signature, etc
  Activated by bootloader
  NCS counterpart is SMP protocol
Download protocol
  Unidirectional, raw data only
  Image size by #XDFUGET command
  Serial Aysnc based on UARTE driver
  Flow control by MTU and pause
    MTU align with UART EasyDMA block size
    Pause to allow MCU Flash write time
  Log-based CRC alignment
    Does not support re-transmit
  MCUBOOT handles versions, image signature, etc
  Activated by MCUBOOT Comments on SMP-based

## Slide 17: Future work
Own partition in flash for download task
Download two images to NCS nRF52 target
MCUBOOT FOTA
  Both the B0 and B1 images needs to be downloaded then judged by nRF52 of which to apply
  Alternatively nRF52 do the check first then download either B0 or B1
nRF53 MCU support
  Application-core only or network-core only DFU is OK with current solution
  Both application and network cores DFU needs revised download protocol
Other MCU support
  The NCS nRF5 solution offers to download one/two images over UART
  Peer side needs its one solution how the image(s) are applied