## Slide 1: Cross DFU Project
Introduction and demo-show
Youqun Sun
H2 2020

## Slide 2: Agenda
Project Brief
  Introduction
  Architecture
Demo Show
  DFU from 91 to 52
  DFU from 52 to 91
Tech Details
  HTTP Download
  DFU bin file format
  app_cmd library
  …

## Slide 3
Project Brief

## Slide 4: Tracker
Web Server
App
Tracker
HTTP
BLE
Notes: Product of picture is from Ruuvi Innovations, Nordic nRF9160 inside.
https://www.nordicsemi.com/News/2019/04/Ruuvi-Node-open-source-node-solution-combines-nRF9160-SiP-and-nRF52840-SoC
Picture is from: https://www.cnx-software.com/2019/04/23/ruuvi-node-open-source-node-solution-nordic-semi-nrf9160-cellular-sip-nrf52840-bluetooth-soc/

## Slide 5: Nordic Inside
Web Server
App
Tracker
HTTP
BLE
UART
nRF91
nRF52
Notes: Product of picture is from Ruuvi Innovations, Nordic nRF9160 inside.
https://www.nordicsemi.com/News/2019/04/Ruuvi-Node-open-source-node-solution-combines-nRF9160-SiP-and-nRF52840-SoC
Picture is from: https://www.cnx-software.com/2019/04/23/ruuvi-node-open-source-node-solution-nordic-semi-nrf9160-cellular-sip-nrf52840-bluetooth-soc/

## Slide 6: Cross DFU
Get DFU file from different way:
  From HTTP (nRF91)
  From BLE (nRF52)
Use case list:
  91 -> 52
  91 -> 91 application
  91 -> 91 modem
  52 -> 52
  52 -> 91 application
  52 -> 91 modem

## Slide 7: Design Architecture
Always store new image in bank 1 of nRF91
Then do:
  DFU to nRF91 by mcuboot
  DFU to nRF52 by secure serial DFU
  DFU to modem by socket

## Slide 8
DFU Procedure: 91 -> 52

## Slide 9: DFU Procedure: 91 -> 52
nRF91
nRF52
Bank 1
Bank 0
Bank 1
Bank 0
UART
1. Download DFU file from web server…
active application
new image
HTTP
Web Server

## Slide 10: DFU Procedure: 91 -> 52
HTTP
nRF91
nRF52
UART
Bank 1
Bank 0
Bank 0
Bank 1
2. Do serial DFU to nRF52…
active application
new image
Web Server

## Slide 11: DFU Procedure: 91 -> 52
HTTP
nRF91
nRF52
UART
Bank 1
Bank 0
Bank 1
Bank 0
3. Copy image in bootloader and set active…
active application
new image
Web Server

## Slide 12
DFU Procedure: 52 -> 91

## Slide 13: DFU Procedure: 52 -> 91
nRF91
nRF52
UART
Bank 1
Bank 0
Bank 1
Bank 0
1. Get DFU file from App and send to 91…
App
BLE
active application
new image

## Slide 14: DFU Procedure: 52 -> 91
nRF91
nRF52
UART
Bank 1
Bank 0
Bank 1
Bank 0
2. Swap active application and new image…
App
BLE
active application
new image

## Slide 15: DFU Procedure: 52 -> 91
nRF91
nRF52
UART
Bank 1
Bank 0
Bank 1
Bank 0
3. Set active for new image…
App
BLE
active application
new image

## Slide 16
DFU Procedure: 52 -> Modem

## Slide 17: DFU Procedure: 52 -> Modem
nRF91
nRF52
UART
Bank 1
Bank 0
Bank 1
Bank 0
1. Get DFU file from App and send to 91…
App
BLE
active application
new image

## Slide 18: DFU Procedure: 52 -> Modem
nRF91
nRF52
UART
Bank 1
Bank 0
Bank 1
Bank 0
2. Copy image to modem core…
App
BLE
active application
new image

## Slide 19: DFU Procedure: 52 -> Modem
nRF52
UART
Bank 1
Bank 0
2. Copy image to modem core…
App
BLE
active application
new image
nRF91
Bank 1
Bank 0

## Slide 20: DFU Procedure: 52 -> Modem
nRF91
nRF52
UART
Bank 1
Bank 0
Bank 1
Bank 0
2. Copy image to modem core…
App
BLE
active application
new image
nRF91
Bank 1
Bank 0
Socket
(modem core)
(app core)

## Slide 21: DFU Procedure: 52 -> Modem
nRF91
nRF52
UART
Bank 0
Bank 1
Bank 0
2. Copy image to modem core…
App
BLE
active application
new image
nRF91
Bank 1
Bank 0
Socket
(modem core)
(app core)
Bank 1

## Slide 22: DFU Procedure: 52 -> Modem
nRF91
nRF52
UART
Bank 1
Bank 0
3. Active new modem image…
App
BLE
active application
new image
nRF91
Bank 1
Bank 0
Socket
(modem core)
(app core)
Bank 1
Bank 0

## Slide 23: Cross DFU Project
It’s a complete system:
  Web server
  nRF91 firmware
  nRF52 firmware
  App
  Script
How do they work?

## Slide 24: Web Server
Upload DFU bin file(*.bin)
Generate a public URL for each uploaded file
http://106.13.189.165/
Based on Flask(Python) web framework
Deployed at Baidu Cloud

## Slide 25: nRF91 Firmware
Use NB-IoT network
Download DFU file from server, HTTP
Do DFU to 52, 91 or modem
Receive file data from nRF52, UART
Based on NCS v1.3.0, http_application_update project
DFU host is ported from Bernard’s project (UartSecureDFU)

## Slide 26: nRF52 Firmware
BLE NUS peripheral
Get DFU file from Mobile App, BLE
Transfer file data to nRF91, UART
Based on SDK v16.0, ble_app_uart project
It requires a serial bootloader

## Slide 27: App
Name: My Toolbox
BLE NUS central
Store DFU file
Transfer DFU file to nRF52, BLE
Based on nRF Toolbox(Android)
A nRF52840 firmware with the same function is implemented as well

## Slide 28: Script
Name: dfu_zip_to_bin.py
Convert a DFU package file(*.zip) to a bin format
Based on Python 3
Usage: $ python dfu_zip_to_bin.py dfu-pkg.zip dfu-bin.bin
Q: Why convert it to bin format?
A: (1) hard to read zip format in MCU (2) 91 and modem DFU files are bin format, unify them

## Slide 29
Demo Show

## Slide 30: Prerequisite
nRF9160 DK
nRF52832 DK
My Toolbox.apk
ncs v1.3.0
sdk v16.0
Python 3

## Slide 31: UART Wire Connection
91 DK
TX: P0.18 RX: P0.17
52 DK
TX: P0.12 RX: P0.11

## Slide 32: UART Wire Connection
91 DK
TX: P0.18 RX: P0.17
52 DK
TX: P0.12 RX: P0.11

## Slide 33: LED and Button of 91 DK
LED 1: NB-IoT network is connected
LED 2: File is downloaded or received
Switch 1 + Switch 2 to left: set URL to 52 DFU file
Switch 1 + Switch 2 to right: set URL to 91 DFU file
Button 1: start to download
Button 2: start to do DFU

## Slide 34: DFU Operation: 91 -> 52
Prepare a new application hex
Generate a DFU package $ python make_dfu_zip.py
Convert to DFU bin file $ python make_dfu_bin.py
Test file
  <cross_dfu>\test\in_files\dfu_bin_52.bin
  Advertising name is Nordic_HRM
Make 52 DFU bin file
Upload to web site
Program 91 and 52 DK
Download DFU file
Do DFU

## Slide 35: DFU Operation: 91 -> 52
Make 52 DFU bin file
Upload to web site
Program 91 and 52 DK
Download DFU file
Do DFU
1
2
3
Access URL of uploaded file: http://106.13.189.165/upload/<uploaded-file-name>

## Slide 36: DFU Operation: 91 -> 52
Update m_http_file_52 variable in main.c
  typically: m_http_file_52 = “upload/<dfu-bin-file>.bin“
Build and program 91 DK
  $ west flash --snr xxxx
Program 52 DK
  Program sd + app + bl + bl_settings
  $ python prog_sd_app_bl.py
Make 52 DFU bin file
Upload to web site
Program 91 and 52 DK
Download DFU file
Do DFU

## Slide 37: DFU Operation: 91 -> 52
Wait NB-IoT connected (LED 1 on)
Put switch 1 and switch 2 to left
Press button 1 to start downloading
When file is downloaded, LED 2 is set on
Make 52 DFU bin file
Upload to web site
Program 91 and 52 DK
Download DFU file
Do DFU

## Slide 38: DFU Operation: 91 -> 52
Press button 2 to start DFU
Check advertising name of 52 DK is changed:
  Cross_DFU_52 -> Nordic_HRM
Make 52 DFU bin file
Upload to web site
Program 91 and 52 DK
Download DFU file
Do DFU

## Slide 39
Demo show: DFU 91 -> 52

## Slide 40: DFU Operation: 52 -> 91
Get firmware bin from project build directory
  .\build\zephyr\app_update.bin
Get modem bin by unzipping modem zip file
  mfw_nrf9160_update_from_1.2.0_to_1.2.0-FOTA-TEST.bin
Test file
  <cross_dfu>\test\in_files\dfu_bin_91.bin
  LED 3 and LED 4 will turn on after booting up
  Welcome message log is Cross DFU Demo(new)
Make 91 DFU bin file
Upload to phone
Program 91 and 52 DK
Transfer DFU file
Do DFU

## Slide 41: DFU Operation: 52 -> 91
Make 91 DFU bin file
Upload to phone
Program 91 and 52 DK
Transfer DFU file
Do DFU
Common method
  Copy file to SD card of your phone
Engineer method (Android only)
  $ adb push <file-name> storage/sdcard0/<dir>

## Slide 42: DFU Operation: 52 -> 91
Build and program 91 DK
  $ west flash --snr xxxx
Program 52 DK
  Program sd + app + bl + bl_settings
  $ python prog_sd_app_bl.py
Make 91 DFU bin file
Upload to phone
Program 91 and 52 DK
Transfer DFU file
Do DFU

## Slide 43: DFU Operation: 52 -> 91
Wait NB-IoT connected (LED 1 on)
My Toolbox
  connect to CROSS_DFU_52
  select DFU bin file
  send image
When file is sent, LED 2 is set on
Make 91 DFU bin file
Upload to phone
Program 91 and 52 DK
Transfer DFU file
Do DFU
1
2
3

## Slide 44: DFU Operation: 52 -> 91
Press button 2 to start DFU
Check changes of 91 DK:
  LED 3 and LED 4 are on
  Welcome message log is updated
Make 91 DFU bin file
Upload to phone
Program 91 and 52 DK
Transfer DFU file
Do DFU

## Slide 45
Demo show: DFU 52 -> 91

## Slide 46: Other Use Cases
91 -> 91, 91 -> modem
  Similar to 91 -> 52
  put switch 1 and switch 2 to right
52 -> 52, 52 -> modem
  Same as 52 -> 91
Skip them to save time

## Slide 47
Tech Details

## Slide 48: Notice
Only useful when you need to use it,
so I will introduce them quickly

## Slide 49
1. HTTP download

## Slide 50: HTTP Download
NCS prepares all things about HTTP download
  HTTP download library
  exchange data with Amazon file storage service
Why not to use a cloud service(dropbox etc.) to store file and download from it?

## Slide 51: GET Request
Generally, use GET request to download file from HTTP server
Suppose a file URL: http://106.13.189.165/dfu_file_91
Get the whole file:
  $ pip install httpie
  $ http GET http://106.13.189.165/dfu_file_91 > dfu_file.bin
How to get the partial content of the file?

## Slide 52: Range Parameter
Use Range parameter in HTTP header to get partial content
For example, get 0 – 10 bytes of the file:
  $ http GET http://106.13.189.165/dfu_file_91 Range:bytes=0-10 > 10_bytes.bin
This feature requires server support
download_client.c library of NCS uses Range parameter
I don’t know who supports it, the direct way is making one

## Slide 53
2. DFU bin file format

## Slide 54: DFU File Types
NCS DFU file
  91 application: xxx.bin
  91 modem: xxx.bin
SDK DFU file
  xxx.zip
It’s better unifying all types of DFU file format

## Slide 55: SDK Zip File Format
DFU package file is made up of:
  manifest.xml
  init packet.dat
  firmware.bin
manifest contains: image name, type and size
We can put init packet and firmware bin together as a bin file and add a header to it

## Slide 56: DFU Bin File Format
Magic Number 1
File Size
Image Count
Init Packet Addr Offset
Init Packet Size
Firmware Addr Offset
Firmware Size
Padding to 128 bytes
Padding to 512 bytes
Firmware
Firmware
Firmware
Magic Number 2
Init Packet content
Init Packet content
Padding to word aligned
CRC32
Image Type
file header
init packet
firmware
crc32

## Slide 57: DFU Bin File Format
Magic Number 1: mcuboot magic number
Magic Number 2: my magic number
File size: binary file size
Image count: always be 1 for this version
Image Type: application or softdevice or bootloader or sd_bl
CRC32: crc 32 for the file, excluding crc field
Use little endian
Padding byte is 0xFF

## Slide 58: File Header of DFU Bin
91 application:
91 modem:
52 DFU:
magic number |  |  |  | padding |  |  | 
3D | B8 | F3 | 96 | xx | xx | xx | xx
magic number |  |  |  | magic number 2 |  |  | 
3D | B8 | F3 | 96 | 51 | 59 | 53 | 49
padding |  |  |  | magic number |  |  | 
xx | xx | xx | xx | 6D | 65 | 44 | 75

## Slide 59
3. app_cmd library

## Slide 60: Introduction
What A library to handle data exchange between two MCUs through UART
Why
  Standardize the process, use request & response to exchange data
  Control the process, handle correct and error operations
  Easy to extend, easy to add customized commands
  Cross the platform, 91 and 52 available
How
  Based on Simple Packet Protocol

## Slide 61: Example
52 asks 91 to erase one flash page
52:
  Define a cmd for this operation
  send cmd to 91
  wait for response
91:
  Define a cmd for this operation
  receive cmd
  process cmd(do erasing)
  respond cmd(send result to 52)

## Slide 62: State Machine

## Slide 63
4. My Toolbox App

## Slide 64: Communication Protocol
Start DFU
  App  52: write 0x00
Get image size
  52  App: notify 0x01
  App  52: write [0x01, 0xFF, 0xFF, 0xFF, 0xFF] (file size in little endian)
Get image data
  52  App: notify 0x02
  App  52: write [0x02, 0xFF, 0xFF, … 0xFF] (129 bytes each packet)
  App  52: write [0x02, 0xFF, 0xFF, … 0xFF] (129 bytes each packet)
  … (repeat 8 times)
Get image data again, until finish

## Slide 65
5. Modem version

## Slide 66: Version Match
Unzip a modem file(*.zip), you can get:
  mfw_nrf9160_update_from_1.2.0_to_1.2.0-FOTA-TEST.bin
  mfw_nrf9160_update_from_1.2.0-FOTA-TEST_to_1.2.0.bin
“mfw_nrf9160_update_from_1.2.0_to_1.2.0-FOTA-TEST.bin”
  Update modem from 1.2.0 to 1.2.0-FOTA-TEST
  If current version is not 1.2.0, updating will be failed
  After updating, new version is 1.2.0-FOTA-TEST

## Slide 67: Get Version
Get version string: mfw_nrf9160_1.2.0
  modem_info_params_get(&modem_info)
  modem_info.device.modem_fw.value_string
Get UUID: 22bd7d7e-368b-4513-aac0-31aa78cafa98
  getsockopt(fd, SOL_DFU, SO_DFU_FW_VERSION, &version, &len);
  snprintf(version_string, sizeof(version_string), "%.*s", sizeof(version), version);

## Slide 68
Thank you