## Slide 1: nRF9160 FOTA Strategy
Nordic Semiconductor
V1.1A

## Slide 2: Firmware updates
Application Firmware
  Full update using MCU Manager
  Max 512 kB image for on-chip swap operation
nRF9160
Application
LTE-M / NB-IoT
Modem
BSD socket
Modem Firmware
  Differential, small size for bug fixes
  Full 2.5 MB update for new features

## Slide 3: Modem firmware
Modem Firmware

## Slide 4: Modem Firmware Versions
Version number structure: a.b.c
  a = Major version
  b = Minor version
  c = Bug fix number
Bug fix number = Bug fix release to earlier delivery.
Minor Version = Feature Release without Application API Break.
Major Version = Feature Release that causes Application API break.

## Slide 5: Modem FOTA Strategy
Delta FOTA Upgrades will be provided between successive bug fix releases.
  For instance:
x.0.0
x.0.1
x.0.2
x.0.3
Delta file 1
Delta file 2
Delta file 3
Delta FOTA updates will not be provided between Feature Releases
x.0.0
x.1.0
x+1.0.0
x.0.1
x.1.1
x+1.0.1
…
…
…
Delta file
Delta file
Delta file
Full new modem firmware image download requires external memory of 3 MB
  Not yet supported by the application

## Slide 6: Modem firmware
Modem Firmware

## Slide 7: Enhanced FOTA
Support download to device with example using HTTP or HTTPS
  Other protocols can be implemented by the customer
nRF Cloud manages devices, firmware and updates
  Host firmware images, versioning and create device update plans
  The user sets up and controls the actual update for the selected devices (AWS Jobs)
  Device Shadow Service that can validate firmware versions in the cloud
  Production offering TBD
MQTT
  MQTT used by nRF Cloud (also AWS, Google Cloud and MS Azure)
  Connects to AWS MQTT broker and subscribes to related AWS Jobs
  Job metadata over MQTT, payload over HTTP
  No solution yet for NB-IoT networks, only supporting UDP
LWM2M
  Verizon ThingSpace and LWM2M_carrier only
  No generic solution available for other clouds/hosts
FOTA support | MQTT | LWM2M (Verizon)
New MCUBoot image | √ | -
New Application image | √ | -
Differential Modem image | √ | √
Full Modem image | - | -

## Slide 8: FOTA over NB-IoT
Most NB-IoT networks do not support TCP communication well
UDP-based transfer protocols are generally supported
Customer should modify the download agent for FOTA to fit with their UDP-based server infrastructure

## Slide 9: Enhanced FOTA cont.
MQTT
HTML/HTMLS
  User/ nRF Cloud services:
  Manage devices
  Manage firmware images
  Control/trigger updates
  Device Shadow Service
  Storage services:
  Host firmware images
  HTTPS:// … URL to image
Application/MCUBoot | Modem
HTTP(S) ‘downloader’ receives new image Complete image is stored in application swap space​ Verifies and authenticates the image Re-boots to swap/replace active application or MCUBoot Encryption planned for future release | HTTP(S) downloader’ receive new image​ Differential image – small size​ Transfer image to modem​ Modem firmware decrypt and authenticate new image Modem re-boots to apply new image​
nRF9160
Application
LTE-M / NB-IoT
Modem
BSD socket

## Slide 10: Serial Device Firmware Update (DFU)
Today w/Thingy:91 and SDK 1.0 features
  Force device into Serial Recovery Mode by holding Thingy:91 button down during reset
  nRF9160 bootloader stops the boot sequence and await new application firmware
  Host sends new firmware over UART (USB through nRF52840 in Thingy:91)
Upcoming in Oct/Nov
  nRF Connect Programmer and nrfjprog updated to support nRF9160 serial recovery and application DFU
Serial DFU controlled from USART
  Standard Zephyr feature that Nordic currently have no example for –similar to FOTA expect for interface (serial vs. HTTP)
  External host sends the new application image over USART
  Application verifies and authenticates the image
  Application Re-boots to swap/replace active application
TBD
  Modem firmware DFU over serial interface
nRF9160
Application
LTE-M / NB-IoT
Modem
BSD socket
LTE
LTE Base station
UART
Host Application
AT commands

## Slide 11: Verizon LWM2M
Current version is 0.6.0
Certified with 1.0.1 modem firmware at Verizon
Mainly supports modem FOTA
Not tested to production quality
Upcoming version is 0.7.0
Will be certified with Verizon on MFW 1.0.1 end of October
Improved feature set
Optional interfaces
Better tested – full release testing with SDK in November